## Slide 1
NETWORK FUNCTION VIRTUALIZATION
and the OSI Architecture
Computer Networks | Seminar Presentation

## Slide 2
What is Network Function Virtualization?
NFV decouples network functions — firewalls, routers, load balancers, NAT, IDS — from proprietary, purpose-built hardware appliances.
These functions are re-implemented as software modules called Virtualized Network Functions (VNFs), running as virtual machines or containers on standard, high-volume servers (COTS hardware).
Standardized by the ETSI NFV Industry Specification Group (ISG) in 2012, initiated by major telecom operators (AT&T, Deutsche Telekom, Orange, etc.).
Core principle: separate the network function (software) from the infrastructure it runs on, enabling deployment, scaling, and migration through software control instead of hardware installation.
Traditional Network
Dedicated hardware boxes
(Router, Firewall, LB, IDS)
one function per appliance
NFV-Enabled Network
Software VNFs on standard
servers — virtual routers,
firewalls, load balancers
Goal: reduce CAPEX/OPEX, speed up service deployment, enable elastic scaling

## Slide 3
NFV Reference Architecture (ETSI MANO)
OSS / BSS (Operations & Business Support Systems)
Virtualized Network Functions (VNF) Layer
vFirewall
vRouter
vLoad
Balancer
vIDS/IPS
Virtualization Layer (Hypervisor / Container Runtime)
NFV Infrastructure (NFVI) — COTS Hardware
Compute
Storage
Network
NFV MANO
Orchestrator (NFVO)
End-to-end service orchestration, network service lifecycle
VNF Manager (VNFM)
Lifecycle management of individual VNFs (instantiate, scale, heal)
Virtualized Infra. Manager (VIM)
Controls & monitors compute, storage, network resources
MANO coordinates orchestration across OSS/BSS, VNFs, and NFVI via standardized reference points

## Slide 4
OSI Architecture and its Relation to NFV
7
Application
6
Presentation
5
Session
4
Transport
3
Network
2
Data Link
1
Physical
The OSI (Open Systems Interconnection) model defines 7 standardized layers for network communication, from physical bit transmission up to application services.
Traditional network appliances are tightly bound to specific layers in dedicated hardware — e.g. switches at Layer 2, routers at Layer 3, and firewalls/load balancers spanning Layers 3–7.
NFV virtualizes these layer-specific functions in software, so a single COTS server can host VNFs operating at multiple OSI layers simultaneously (e.g. a virtual switch at L2 and a virtual firewall at L3–L7).
The Virtualization Layer / hypervisor effectively sits below Layer 1–2 of the VNF's view, presenting virtual NICs and virtual links that emulate the physical/data-link layers to the guest VNF.
This decoupling allows network services to be composed as a chain of VNFs (Service Function Chaining) that jointly implement multi-layer processing, independent of underlying hardware topology.

## Slide 5
Benefits, Challenges & Conclusion
Benefits
Reduced CAPEX/OPEX — commodity servers replace costly proprietary appliances
Rapid service deployment and elastic, on-demand scaling of network functions
Vendor independence and flexible multi-tenant network operation
Simplified upgrades — software updates instead of hardware replacement
Challenges
Performance overhead from virtualization compared to dedicated hardware
Complex orchestration and management across multi-vendor VNFs (MANO)
Security concerns from shared, multi-tenant virtualized infrastructure
Interoperability and standardization across different NFV platforms
Conclusion: NFV transforms rigid, layer-bound hardware appliances into flexible software functions, reshaping how OSI-layer network services are deployed, managed, and scaled.